## Slide 1: GENI Operations: Monitoring
David P. Wiggins, GPO
GEC20: June 23, 2014

## Slide 2: Monitoring Architecture Overview
Network
Provider
Local DS
Local DS
Compute Aggregate
Network
Aggregate
Clearing House
Collector
Alerting
Reports
Collector
Local DS
Local DS
Collector
Alerting
Visualization
Reports
Internet
(Control Plane)
External
Checks
Local DS
Polling REST calls
JSON responses
Not a GENI aggregate!
Notes: Explain not a full set of arrows
Configuration may not be a local DS, configuration for

## Slide 3: Monitored Objects
Aggregates
Slices
Slivers
Users
Authorities
Nodes
Interfaces
Interface-VLANs
Links

## Slide 4: What is a link?
= endpoint of a link represented by an interfacevlan, which must then reference a valid interface. The vlan must be the same on both sides of a link.
Network Aggregate
Node 1
AM
Node 2
Compute Aggregate 1
Switch
Local DS
Node 3
Local DS
Compute Aggregate 2
Switch

## Slide 5: Progress
Release 1.0 ops-monitoring software on May 1
  Now at 1.1 patch 2
Many datastores and collectors are coming online
Working through issues with
  the API
  the implementation
  the data coming back from the datastores

## Slide 6: Deployments
Instageni |  | ExoGENI | Network/Other | Collector
utah-ig utahddc-ig uky-ig princeton-ig kansas-ig nyu-ig max-ig nysernet-ig illinois-ig missouri-ig rutgers-ig stanford-ig cornell-ig lsu-ig cwru-ig moxi-ig | nps-ig idaho-ig ucla-ig osu-ig umkc-ig uchicago-ig ohmetrodc-ig northwestern-ig gpo-ig kettering-ig gatech-ig clemson-ig sox-ig wisconsin-ig utah-pg | rcivmsite bbnvmsite uva-nlvmsite osfvmsite slvmsite ucdvmsite uflvmsite wvnvmsite ncsuvmsite uhvmsite fiuvmsite nictavmsite | al2s.net.internet2.edu ion.internet2.edu of.internet.edu externalcheck/gpo ch.geni.net | GPO U Kentucky

## Slide 7: Global Report Plot

## Slide 8: Plot of Node Stats

## Slide 9: Plot of Slice/Sliver Association

## Slide 10: Future Work
Improve API (REST/JSON) specification
  Scalability/performance
  Consistency
  Semantic clarity
Support additional measurements
Improve the reference implementation
  Datastore robustness
  Collector completeness, scalability, ease of use
Wider production deployment

## Slide 11: Thanks!
ExoGENI: Jonathan Mills, Victor Orlikowski, Ilya Baldin
Internet2: A.J. Ragusa
GMOC: Chad Kotil
InstaGENI: Gary Wong, Leigh Stoller
MAX: Tom Lehman, Xi Yang
UKY: Cody Bumgardner, Caylin Hickey
GPO: Ryan Irwin, Stéphane Blais, Ali Sydney, Heidi Picher Dempsey

## Slide 12: Backup slides
Backup slides

## Slide 13: What is a link?
Compute Aggregate 1 must advertise this link. We omit the physical port on the switch to which the node is directly connected.
Network Aggregate
Node 1
AM
Node 2
Compute Aggregate 1
Switch
Local DS
Node 3
Local DS
Only dataplane links are reported, i.e., links that are part of an experiment and thus can carry experiment traffic. Endpoints of such links are not usually reachable from the arbitrary places on the Internet, in contrast to the control plane.
Compute Aggregate 2
Switch
Both the compute AM and the network AM advertise this link. Each side must know the exact URN of the interface and interface-vlan of the other side.
= endpoint of a link represented by an interfacevlan, which must then reference a valid interface. The vlan must be the same on both sides of a link.
Interface on the node (may be a VM)
If there are transit networks on this path that do not run GENI monitoring, they are either omitted or expressed as an L2 (layer 2) path. Transit networks that do run GENI monitoring will appear as link endpoints.
egress interface from rack to the outside world. Ingress/egress are from the point of view of traffic going from Compute Aggregate 1 to 2.
egress interface from the network aggregate
The network AM advertises this link. It is strongly encouraged to include an L2path giving the details of the path between the ingress and egress interfaces.
This switch connects the rack to the outside world. Rack AMs such as this compute AM must advertise this switch as a node so that we have a place to put its interfaces and interface-vlans.
ingress interface into the network aggregate

## Slide 14: Sample Collected Data
collector=> select id, urn from ops_link_interfacevlan where link_id = 'ion.internet2.edu-100021' ;
id | urn
------------------------------------------------------------+-------------------------------------------------------------------------
ion.internet2.edu/rtr.salt.ion.internet2.edu/ge-10/2/7/885 | urn:publicid:IDN+ion.internet2.edu+interface+rtr.salt:ge-10/2/7:protogeni:885
ion.internet2.edu/rtr.newy.ion.internet2.edu/xe-0/2/2/305 | urn:publicid:IDN+ion.internet2.edu+interface+rtr.newy:xe-0_2_2:*:305
(2 rows)
collector=> select tag, interface_urn from ops_interfacevlan where id = 'ion.internet2.edu/rtr.salt.ion.internet2.edu/ge-10/2/7/885' ;
tag | interface_urn
-----+---------------------------------------------------------------------------
885 | urn:publicid:IDN+ion.internet2.edu+interface+rtr.salt:ge-10/2/7:protogeni
(1 row)
collector=> select id, properties$role, properties$max_bps from ops_interface
where urn = 'urn:publicid:IDN+ion.internet2.edu+interface+rtr.salt:ge-10/2/7' ;
id | properties$role | properties$max_bps
--------------------------------------------------------+-----------------+--------------------
ion.internet2.edu/rtr.salt.ion.internet2.edu/ge-10/2/7 | transport | 1000000
(1 row)
This demonstrates tracing from a link to its interfacevlans to its interfaces.