## Slide 1: GENI Monitoring Meeting
Stéphane Blais and David P. Wiggins, GPO
GEC21, October 22, 2014
At the GPO Office, Hoosier Room, IMU Main Level, 4-5:30 PM

## Slide 2: Agenda
Possible new development
  Database schema changes
  JSON schema changes
  Other new features
Discussion of existing monitoring data
  Inter-aggregate links
  Stats for interfacevlans
  Alerting with messy data

## Slide 3: Possible Database Schema Changes
Field | Change?
$schema | Remove. rest_call_handler should control this.
id | Remove? urn is good enough?
selfRef | Remove. rest_call_handler can fill this in.
urn | Leave as-is
ts | Leave as-is
tag | Leave as-is
interface_urn | Leave as-is
interface_href | Remove. rest_call_handler can fill this in.
Using the ops_interfacevlan table as a representative example:
These changes:
Eliminate many data redundancies
Simplify the task of understanding and populating the tables
Apply to both object and relationship tables

## Slide 4: Sample JSON response to data query
[
{"tsdata":[
{"ts":1412124480000000,"v":7917},
{"ts":1412124600000000,"v":7026},
{"ts":1412125320000000,"v":8731}],
"eventType":"ops_monitoring:rx_bps”,
"subject": “https://gmoc-db.grnoc.iu.edu/info/interface/ion.internet2.edu/xe-0/2/2”
"id":"rx_bps:ion.internet2.edu+interface+rtr.wash.ion.internet2.edu:xe-0/2/2",
"description":"bits per second received on this interface",
"units":"float",
"$schema": “http://www.gpolab.bbn.com/monitoring/schema/20140828/data#”
},
{“tsdata”:[….] }
]
For reference, this is what a typical response to a data query currently looks like. We will look at some possible changes to this format in the next slides.

## Slide 5: JSON data response: top-level list
[ does not match data schema (schema does not start with a list)
{"tsdata":[
{"ts":1412124480000000,"v":7917},
{"ts":1412124600000000,"v":7026},
{"ts":1412125320000000,"v":8731}],
"eventType":"ops_monitoring:rx_bps”,
"subject": “https://gmoc-db.grnoc.iu.edu/info/interface/ion.internet2.edu/xe-0/2/2”
"id":"rx_bps:ion.internet2.edu+interface+rtr.wash.ion.internet2.edu:xe-0/2/2",
"description":"bits per second received on this interface",
"units":"float",
"$schema": “http://www.gpolab.bbn.com/monitoring/schema/20140828/data#”
},
{“tsdata”:[….] }
]
Currently, the response is a list [ ] of JSON objects each of which conform to the data schema. The response as a whole does NOT pass JSON validation. Special-case validation code is needed for this one response. Ideally, the entire response would pass JSON validation without special treatment.

## Slide 6: JSON data response: top-level list FIX
{
"$schema": http://www.gpolab.bbn.com/monitoring/schema/20141205/data#
“measurements”: [
{
"tsdata":[
{"ts":1412124480000000,"v":7917},
{"ts":1412124600000000,"v":7026},
{"ts":1412125320000000,"v":8731}],
"eventType":"ops_monitoring:rx_bps”,
"subject": “https://gmoc-db.grnoc.iu.edu/info/interface/ion.internet2.edu/xe-0/2/2”
"id":"rx_bps:ion.internet2.edu+interface+rtr.wash.ion.internet2.edu:xe-0/2/2",
"description":"bits per second received on this interface",
"units":"float”,
},
{“tsdata”:[….] }
]
}
$schema only appears once in the entire response
No impact on database table population
Collectors must parse new format

## Slide 7: JSON data response: timestamps
[
{"tsdata":[
{"ts":1412124480000000,"v":7917},
{"ts":1412124600000000,"v":7026},
{"ts":1412125320000000,"v":8731}],
"eventType":"ops_monitoring:rx_bps”,
"subject": “https://gmoc-db.grnoc.iu.edu/info/interface/ion.internet2.edu/xe-0/2/2”
"id":"rx_bps:ion.internet2.edu+interface+rtr.wash.ion.internet2.edu:xe-0/2/2",
"description":"bits per second received on this interface",
"units":"float",
"$schema": “http://www.gpolab.bbn.com/monitoring/schema/20140828/data#”
},
{“tsdata”:[….] }
]
Timestamps could probably be milliseconds instead of microseconds
Could reduce the response size significantly
We would want to make this change across the entire schema for consistency
Database populators would need to change to store milliseconds
Collectors would have to deal with both time granularities for a while, facilitated by schema versioning

## Slide 8: JSON data response: ops_monitoring prefix
[
{"tsdata":[
{"ts":1412124480000000,"v":7917},
{"ts":1412124600000000,"v":7026},
{"ts":1412125320000000,"v":8731}],
"eventType":"ops_monitoring:rx_bps”,
"subject": “https://gmoc-db.grnoc.iu.edu/info/interface/ion.internet2.edu/xe-0/2/2”
"id":"rx_bps:ion.internet2.edu+interface+rtr.wash.ion.internet2.edu:xe-0/2/2",
"description":"bits per second received on this interface",
"units":"float",
"$schema": “http://www.gpolab.bbn.com/monitoring/schema/20140828/data#”
},
{“tsdata”:[….] }
]
ops_monitoring prefix seems unnecessary. Remove it.
Also remove it in the REST call that queries for this data
No impact on database population
Collectors would see different eventType strings, but it shouldn’t matter?

## Slide 9: JSON data response: subject field
[
{"tsdata":[
{"ts":1412124480000000,"v":7917},
{"ts":1412124600000000,"v":7026},
{"ts":1412125320000000,"v":8731}],
"eventType":"ops_monitoring:rx_bps”,
"subject": “https://gmoc-db.grnoc.iu.edu/info/interface/ion.internet2.edu/xe-0/2/2”
"id":"rx_bps:ion.internet2.edu+interface+rtr.wash.ion.internet2.edu:xe-0/2/2",
"description":"bits per second received on this interface",
"units":"float",
"$schema": “http://www.gpolab.bbn.com/monitoring/schema/20140828/data#”
},
{“tsdata”:[….] }
]
Our schema convention is to use the _href suffix for fields that contain URLs, so add that here
Diverges from UNIS schema, but we have been moving away from UNIS
No impact on database population
Collectors must parse new format

## Slide 10: JSON data response: id field
[
{"tsdata":[
{"ts":1412124480000000,"v":7917},
{"ts":1412124600000000,"v":7026},
{"ts":1412125320000000,"v":8731}],
"eventType":"ops_monitoring:rx_bps”,
"subject": “https://gmoc-db.grnoc.iu.edu/info/interface/ion.internet2.edu/xe-0/2/2”
"id":"rx_bps:ion.internet2.edu+interface+rtr.wash.ion.internet2.edu:xe-0/2/2",
"description":"bits per second received on this interface",
"units":"float",
"$schema": “http://www.gpolab.bbn.com/monitoring/schema/20140828/data#”
},
{“tsdata”:[….] }
]
The id field does not need to start with the event (rx_bps here)
  The event is already available as eventType
  id no longer directly references the relevant object; this is confusing
No impact on database population
Collectors must parse new format

## Slide 11: JSON data response: $schema field
[
{"tsdata":[
{"ts":1412124480000000,"v":7917},
{"ts":1412124600000000,"v":7026},
{"ts":1412125320000000,"v":8731}],
"eventType":"ops_monitoring:rx_bps”,
"subject": “https://gmoc-db.grnoc.iu.edu/info/interface/ion.internet2.edu/xe-0/2/2”
"id":"rx_bps:ion.internet2.edu+interface+rtr.wash.ion.internet2.edu:xe-0/2/2",
"description":"bits per second received on this interface",
"units":"float",
"$schema": “http://www.gpolab.bbn.com/monitoring/schema/20140828/data#”
},
{“tsdata”:[….] }
]
Don’t need to repeat $schema in every block of tsdata
Already addressed in top-level list fix in a previous slide
No impact on database population
Collectors must parse new format

## Slide 12: Revised JSON response to data query
{
"$schema":http://www.gpolab.bbn.com/monitoring/schema/20140828/data#
“measurements”: [
{
"tsdata":[
{"ts":1412124480000,"v":7917},
{"ts":1412124600000,"v":7026},
{"ts":1412125320000,"v":8731}],
"eventType":”rx_bps”,
"subject_href":https://gmoc-db.grnoc.iu.edu/info/interface/…”
"id":”ion.internet2.edu+interface+rtr.wash.ion.internet2.edu:xe-0/2/2",
"description":"bits per second received on this interface",
"units":"float",
},
{“tsdata”:[….] }
]
}
Combining all of these changes, we get something like this:

## Slide 13: Other Possible JSON Schema Enhancements
Bidirectional navigation
  Nodes list their interfaces, but interfaces don’t specify their node. Fix all such instances of this.
  Allows lightweight navigation of the monitoring data without needing to collect and store all of the data first
  This is a sweeping change that dwarfs any of the other JSON schema changes that have been discussed
Wildcard for event types in data queries
  Objects can already be wildcarded, so this completes the feature
  Gotchas with datastores supporting multiple aggregates
Objects could specify what measurements they support
  Would make querying data more straightforward
Node schema
  Associate VMs with the physical machines they’re running on
  Add a baremetal node type

## Slide 14: Possible new features
OpenFlow support
  New flowspace resource type? What’s in a flowspace resource?
  Adding this is a certainty, not just a possibility
Flexible install location
  instead of requiring /usr/local/ops-monitoring
Release packaging (RPM, .deb, BSD pkg)
Documentation

## Slide 15: Discussion of existing monitoring data
Representation of inter-aggregate links
Providing statistics for interfacevlans
Alerting in the presence of absent, stale, or incorrect data